## Slide 1: EMV
Erik Poll
Digital Security

## Slide 2: Payment fraud in Netherlands (Meuro)
Source: Dutch Payment Association and Nederlandse Vereniging van Banken (NVB) https://www.bankinbeeld.nl/thema/veiligheid/
phishing
stolen/lost bank card
credit card
total
help desk fraud

## Slide 3: Payment fraud in Netherlands (Meuro)
Source: betaalvereniging.nl and nvb.nl

## Slide 4: Payment fraud in Netherlands – longer term trends
incl. skimming, stolen & lost cards
incl. malware & phishing

## Slide 5: Overview
The EMV standard
  Known issues with EMV
EMV contactless
Formalisation & Verification of EMV using F# and ProVerif
EMV-CAP for internet banking
Conclusions

## Slide 6: EMV
Started 1993 by EuroPay, MasterCard, Visa
Common standard for communication between
  smartcard chip in bank card (aka ICC)
  terminal (POS or ATM)
  issuer back-end
Specs controlled by which is owned by
Billions of cards in use
Also contactless and on mobile phone

## Slide 7: Motivation for EMV chip: skimming
Magnetic stripe (mag-stripe) on bank card can contain digitally signed information
but... this info can be copied

## Slide 8: Skimming equipment
Fake keyboard
to intercept PIN code
Fake cover
that copies magnetic stripe

## Slide 9: Skimming equipment for NS terminals

## Slide 10: Skimming in the Netherlands
    [Source: NVB/Betaalvereniging]
Drop due to
better monitoring, detection, and reaction (esp. blocking cards)
introduction of EMV (2012)
geoblocking (2013)
Chart: Fraud (million €)
| 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019
Skimming fraud (million euro) | 15 | 31 | 36 | 20 | 39 | 29 | 6.8 | 1.3 | 1.6 | 1.5 | 1.5 | 1.2 | 1.45

## Slide 11: Does EMV chip reduce skimming?
UK introduced EMV in 2006
USA is still migrating to EMV, and criminals have moved there...
 | 2005 | 2006 | 2007 | 2008
domestic | 79 | 46 | 31 | 36
 | 2005 | 2006 | 2007 | 2008
domestic | 79 | 46 | 31 | 36
foreign | 18 | 53 | 113 | 134
Skimming fraud with UK cards, in millions ₤ [Source: Payments UK]

## Slide 12: Liability shifts
Move to EMV chip involves liability shifts
Customer liable for fraud with their PIN code
Vendors liable for fraud if they still use magstripe
    In the USA, for POS starting Oct 2015, for ATMs Oct 2017, for petrol stations Oct 2020.

## Slide 13
The EMV standard

## Slide 14: The EMV protocol suite
EMV is not a protocol, but a toolkit of building blocks for protocols with
  3 card authentication mechanisms
    SDA, DDA, CDA
  5 cardholder verification mechanisms
    online PIN, offline plaintext PIN, offline encrypted PIN, handwritten signature, no card holder verification
  2 types of transactions: offline, online
  All mechanisms again parameterised by Data Object Lists (DOLs)
Specs public but very complex (4 books, >750 pages)
  Specs do not motivate design or mention security objectives…

## Slide 15: EMV protocol phases
Initialisation
  Terminal reads some data from the card, incl. several DOLs
Card Authentication (using SDA, DDA or CDA)
Cardholder Verification (optional, for instance using PIN)
Terminal & Card Risk Management
Transaction
  where the card produces Application Cryptogram (AC)
  with HMAC calculated with shared symmetric key
  NB terminal does not have this key, so it cannot authenticate cryptograms when it is offline

## Slide 16: Parameterisation using DOLs
Data Object Lists specify a list of data elements
  eg amount, currency, primary account number (PAN), application transaction counter (ATC), card/terminal-generated nonce (UN), …
Cards contain several DOLs that specify
  data elements required as input to the card
  data elements included in HMACs produced by the card
NB this means the protocol is still fully configurable. Eg including the amount and currency in the HMAC makes sense, but is not required.

## Slide 17: EMV key set-up
Card & issuer have a shared symmetric key (3DES or AES) used to compute HMACs on transactions
  Terminal does not have this key, so cannot check these
Issuer has private RSA key and terminal knows public key
  This allows SDA: terminal authenticates static signed data on the card
(Optional) DDA & CDA cards have a private RSA key and associated certificate, signed by issuer
  Card can now sign dynamic data that terminals can authenticate
    to authenticate card or transaction

## Slide 18: II. Card Authentication: SDA
SDA – Static Data Authentication
  SDA card cannot do asymmetric crypto
  Card presents static data (card no, expiry date etc) signed by issuer ie. card no, expiry date, ...++ { hash(card no, …) }PRIVKEY-ISSUER
  Problem: can be replayed, so card can be cloned
    Of course, clone will always say offline PIN check succeeded
  Hence: offline terminal can be fooled
    Transaction is signed (MACed) using symmetric key, but terminal cannot check this MAC
    Issuer will spot this fraud later
SDA is being phased out; Visa & Mastercard forbid issuance of offline capable SDA cards since 2011

## Slide 19: II. Card Authentication: DDA
SDA – Static Data Authentication
DDA – Dynamic Data Authentication
  Card has (Pub,Priv) keypair and does challenge-response
    This requires more expensive card than SDA: one that can do asymmetric crypto
  Security flaw : card authenticated, but not the transaction
  Hence: offline terminal can still be fooled
    Attacker can let the terminal authenticate the card but then spoof the subsequent transaction data with its HMAC using some MitM device
    Issuer will spot fraud later

## Slide 20: II. Card Authentication: CDA
SDA – Static Data Authentication
DDA – Dynamic Data Authentication
CDA – Combined Data Authentication
  Card has (Pub,Priv) keypair, as in DDA
  Signature now added over all the transaction data
    so now an offline terminal can check the authenticity of the card and of the transactions

## Slide 21: II. Card Authentication
SDA – Static Data Authentication
DDA – Dynamic Data Authentication
CDA – Combined Data Authentication
Most cards in use today are DDA

## Slide 22: III. Cardholder Verification Methods (CVMs)
PIN
  online: PIN checked by the issuer
  offline: PIN checked by the chip
    b1. unencrypted
    PIN could be eavesdropped using shim
    b2. encrypted
    requires a card that can do asymmetric crypto
Handwritten signature
Nothing
NB: only offline PIN involves the smartcard chip; Dutch bank cards typically do online PIN

## Slide 23: Cardholder Verification Methods (CVM)
Terminal and smartcard negotiate which CVM is used
  given their list of rules that specify allowed/supported method, in order of preference, with conditions
  Eg. transactions at tollroads do not require PIN, (contactless) payments under certain aim do not require PIN, …
Potential for trouble: forcing terminal/card to fall back to a weak CVM

## Slide 24: conditions for applying specific CVM method

## Slide 25: V. Transaction
For the transaction the card generates cryptograms
  ie data with HMAC, and for CDA-cards, also a digital signature
For offline transactions the card just generates one cryptogram (TC)
For online transactions the card generates 2 cryptograms
  Card generates a first cryptogram (ARQC) that the terminal forwards to the issuing bank
  Bank sends a reply which the terminal forwards to the card
    telling the card to go ahead or not
  Card generates second cryptogram (TC) confirming the transaction, provided the bank gave approval

## Slide 26: V. Transaction
The data is included in the cryptograms is configured by DOLs (Data Object Lists)
It typically includes
  the amount
  a terminal-generated nonce (aka Unpredictable Number)
  the card’s Application Transaction Counter (ATC)
    a counter that is increased with each transaction
currency | amount | ATC | UN | HMAC = Enc(hash(currency, amount, ATC, UN))

## Slide 27: EMV limitations & troubles…

## Slide 28: Man-in-the-Middle attacks
Passive eavesdropping and active MitM possible with a shim
Two abuse scenarios
  tampering with a terminal
  shim invisible in terminal for MitM attack
  tampering with a card, which is then used at normal terminal
eg acting as relay of (stolen?) genuine card to a terminal

## Slide 29: Already discussed
SDA cards can be cloned
  Fundamental limitation due to absence of asymmetric crypto on SDA cards
  NB back in the 1990s it was, but nowadays speed or costs are no longer valid excuses not to use ssymmetric
DDA card cannot be cloned, but with a DDA card we can fool the terminal into accepting a bogus offline transaction
  Stupid design decision to only use the asymmetric key to authenticate the card and not also the transaction

## Slide 30: 3. Backwards compatibility...
Track 2 magstripe data is also used by the EMV chip, so after eavesdropping on (unencrypted!) chip-terminal communication an attacker can reconstruct the magstripe
If the card uses offline plaintext PIN, attacker can also eavesdrop the PIN, so attacker does not need a camera
First incident with tampered EMV-CAP readers inside Dutch ABN-AMRO bank branches
  Criminals caught & convicted in 2011
EMV specs have been updated to avoid this

## Slide 31: 4. Offline PIN: spot the security problem!
Terminal can choose to do offline PIN, ie. ask the card to check the PIN
The OK response is simply the status word 0x9000
PIN
PIN
OK!

## Slide 32: 4. Offline PIN: spot the security problem!
Terminal can choose to do offline PIN, ie. ask the card to check the PIN
The OK response is simply the status word 0x9000
Problem: OK response is not authenticated so terminal can be fooled by a Man-in-the-Middle attack
The cryptogram will reveal the transaction was PIN-less, so the bank will later know the PIN was not entered
[Stephen Murdoch et al., Chip & PIN is broken, FC’2010]
Reportedly won’t work in NL, as Dutch cards always go online for PIN check
PIN
PIN
OK!

## Slide 33: Criminal use of this ‘PIN OK’ attack
Tampered cards used by criminal gang: chips from stolen cards inserted under another chip that carries out MitM attack to fake ‘PIN OK’ response
[Houda Ferradi et al., When Organized Crime Applies Academic Results: A Forensic Analysis of an In-Card Listening Device, Journal of Cryptographic Engineering, 2015]
xray reveals
green stolen chip under
blue microcontroller

## Slide 34: 5. Rollback to unencrypted PIN
Shim can force a rollback to unencrypted PIN, by modifying card response to indicate the card does not support it
Strangely, the terminal can tell the card is lying, as the signature over static card data is incorrect, but it does not abort the transaction!
[Barisani et at, Chip & PIN is definitely broken, DEFCON 2011]
Impact limited because
  just having the PIN of a DDA card is useless without the card
  the attack is detectable in the back-end
Reportedly, most terminals in NL patched to disallow this rollback
We tried this attack, and bank detected it almost in real time
  the one terminal we tried had not been patched…

## Slide 35: 6. Bad random number generation
Successive 32 bit random numbers in the log of a Maltese ATM
F1246E04
F1241354
F1244328
F1247348
This weak random number could be abused:
attacker with temporary access to card can copy static data and
record enough responses to make a clone (pre-play attack)
[Bond et al. , Chip and Skim: cloning EMV cards with the pre-play attack, CHES 2012]
More information about criminal ATM hacks:
https://blog.kaspersky.com/sas-2017-atm-malware/14509, April 2017
https://darknetdiaries.com/episode/35/

## Slide 36: Stealing PIN codes using infrared?
Claims of attacks using infra-red camera to observe PIN
[Source: iPhone ATM PIN code hack, https://www.youtube.com/watch?v=8Vc-69M-UWk]

## Slide 37: Stealing PIN codes using infrared?
These claims are bogus!
Dutch police and national TV programs (Tros Opgelicht & Opsporing Verzocht) believed this bogus story.
https://www.politie.nl/gezocht-en-vermist/gezochte-personen/2016/januari/09-oost-brabant/09-diefstal-pinpas-en-nieuwe-methode-pinpasfraude.html
For computer keyboards it has proven possible: ‘Thermanator: Thermal Residue-Based Post Factum Attacks on Keyboard Data Entry’, Asia CCS 2019, https://doi.org/10.1145/3321705.3329846
Thermal images we took after entering 2 different PINs

## Slide 38: Inferring PIN code from (covered) hand movements
Machine Learning models can be trained to recover PIN code from movements of covered hand
Matteo Cardaioli, Stefano Cecconello, Mauro Conti, Simone Milani, Stjepan Picek, and Eugen Saraci ‘Hand Me Your PIN! Inferring ATM PINs of Users Typing with a Covered Hand’, USENIX Security, 2022

## Slide 39: Contactless payments

## Slide 40: Contactless EMV
with ISO/IEC 14443 contactless or dual contact card
or NFC mobile phone
Instead of one generic spec, as for contact payments, there are
individual specs for each of the 10 versions
  in 10 books, > 2000 pages
Same building blocks as original contact spec, but some efforts to minimize the number of messages

## Slide 41: Security challenge with mobile phones
Where to securely store keys & PIN?
Where do compute MACs & signatures using these keys?
Solutions include
Use the SIM card Briefly tried by Rabobank, but national scheme with all banks & telcos abandoned
Using secure hardware in the phone: Apple Secure Enclave on iPhone, hardware-backed keystore (aka Strongbox Keymaster) on Android
Store keys in main memory & use the normal processor
  Possible security enhancements:
  using white-box crypto to obfuscate key material
  have symmetric key that can only be used for one transaction, so that app needs a new key for each transaction, aka EMV Tokenization
Use of biometric authentication on phones can offer security advantage over smartcard.

## Slide 42: Security & privacy worries
Contactless payments, without PIN, seem insecure…
Who uses a metal container to shield their contactless bank card?
Who has asked their bank to disable contactless payments for their card?
Who thinks that contactless payments without PIN is less secure than contact payment with PIN?

## Slide 43: Passive attacks on contactless cards
Eavesdrop on wireless communication between terminal & card
  This is possible at 10-20 meters
Eavesdropping only poses a small privacy risk:
  The communication reveals eg. your bank account nr
  (Recall that most EMV communication is unencrypted)

## Slide 44: Active attacks on contactless cards
Secretly activate card in someone’s pocket (aka digital pickpocketing)
  This is only possible at 40-50 cm because activating the card requires a strong magnetic field
        [René Habraken et al., An RFID Skimming Gate Using Higher Harmonics, RFIDSec 2015]

## Slide 45: Active relay attack on EMV contactless
Active attacker can do a relay attack
But is there a good criminal business model? Probably not…
Relay attacks normally require very fast relay (< 200 msec) or else a time-out occurs.
Time-out of contactless payment terminal:
> 50 seconds
Improvement in EMV protocol now includes distance bounding - ie. time-critical - step, but it will be many years before this ever gets implemented in cards & terminals

## Slide 46: Risks of PIN-less contactless payments?
Risks of contactless payment without PIN
  You loose max. € 50 if your card is stolen
  You loose max. € 25 euro if you fall victim to a relay attack
  Dutch banks typically cover these losses.
Risks of contact payment with PIN
  You don’t loose any money if your card is stolen
  You can loose €1000 or more if your card is stolen after attacker snooped your PIN code
  Banks will typically not cover these losses…
So the ‘extra security’ of the PIN probably increases risk for customers.
As always: technical security weakness ≠ risk
where risk = likelihood x impact

## Slide 47: Some flaws our students found
Mistake in most first generation Dutch contactless cards:
  functionality to check the PIN code offline, which should only be accessible via the contact interface was also accessible via the contactless interface
Possible risk for DoS attacks, rather than financial fraud?
Flaw discovered by Anton Jongsma, Robert Kleinpenning, and Peter Maandag.
Contactless payment terminals of one manufacturer could be crashed with a legal – but unusual – input
  namely an extended length APDU
  Flaw discovered by Jordi van den Breekel
  Why are terminals not tested better as part of certification?
A Security Evaluation and Proof-of-Concept Relay Attack on Dutch EMV Contactless Transactions

## Slide 48: EMV contactless: Backwards compatibility
Early contactless cards suffered from two problems due to backwards compatibility problems
Very early contactless credit cards reported magstripe data unencrypted over the air, so magstripe clone can be made
  [Heydt-Benjamin et al, Vulnerabilities in First-Generation RFID-enabled Credit Cards, FC 2007]
Later contactless credit cards use a dynamically generated 3 digit code to replace the 3 digit CVC code. But 3 digits is not a lot of entropy, so codes can be harvested & replayed
  [M. Roland et al. Cloning Credit Cards: A combined pre-play and downgrade, WOOT 2013]

## Slide 49: Formalising & Verifying EMV
[Joeri de Ruiter and Erik Poll, Formal analysis of the EMV protocol suite, TOSCA 2011]

## Slide 50: Complexity of the EMV specs
Specs too complex to understand
  long specs, split over 4 books, > 750 pages
    for contactless: another 10 books, > 2000 pages
  little or no discussion of security goals or design choices
  little abstraction or modularity

## Slide 51: Problem: complexity
One sample sentence taken from these thousands of pages
  “If the card responds to GPO with SW1 SW2 = x9000 and AIP byte 2 bit 8 set to 0, and if the reader supports qVSDC and contactless VSDC, then if the Application Cryptogram (Tag '9F26') is present in the GPO response, then the reader shall process the transaction as qVSDC, and if Tag '9F26' is not present, then the reader shall process the transaction as VSDC.”

## Slide 52: Formalising EMV ?
Can formal techniques for security protocol analysis with tools like ProVerif cope with EMV?
First attempt: formalising EMV in ProVerif
Horrible! Case distinctions in applied pi-calculus cause lots of duplication
Beware: real protocols always involve multiple variants, so in ProVerif people typically only verify one variant, leaving out options & abstracting away from lots of messy details…
Second attempt: formalising EMV in F#
Much better! F# allows sequential if-statements & functions

## Slide 53: Formalisation of EMV
(Known) security flaws can now be found automatically by
FS2PV & Proverif tool for security protocol verification

## Slide 54: Formalisation of EMV in F#
EMV can be formalised in 370 lines of F# code
  including all options
    SDA, DDA, CDA
    any card holder verification mechanism
    off/online transations
  But DOLs has to be fixed
    Model uses minimal assumptions on DOLs taken from Dutch bank & credit cards
    Hardcoded in the model, but could easily be changed

## Slide 55: Part of EMV model: DDA
// Perform DDA Authentication if requested, otherwise do nothing
let card_dda (c, atc, (sIC,pIC), nonceC) dda_enabled =
let data = Net.recv c in
if Data.INTERNAL_AUTHENTICATE = APDU.get_command data then
if dda_enabled then
begin let nonceT = APDU.parse_internal_authenticate data in
let signature = rsa_sign sIC (nonceC, nonceT) in
Net.send c (APDU.internal_authenticate_response nonceC signature);
Net.recv c
end
else failwith "DDA not supported by card"
else data

## Slide 56: Analysis of the F# model
F# can be translated to pi calculus by FS2PV tool and then analysed using ProVerif
Translation to pi calculus explodes things a bit
  370 lines of F# becomes 3 kloc of pi calculus
But… ProVerif can still verify security properties
  usually in minutes, but this requires some care!

## Slide 57: Properties checked with ProVerif
Sanity checks to ensure absence of deadlock
Secrecy of private keys
Highest supported card authentication method is used
  eg no fallback to say SDA can be forced
‘transaction security’: if a transaction is completed, then everyone agrees on the parameters (eg with/without pin, off/online, amount,…)
query evinj:TerminalTransactionFinish(sda,dda,cda,pan,amount,…)
==> evinj:CardTransactionInit(sda,dda,cda,pan,amount,…)
No new attacks found, but most existing attacks inevitably (re)discovered

## Slide 58: EMV-CAP

## Slide 59: EMV CAP protocol
EMV chip used for internet banking or e-commerce
  challenge-response mechanism using the bank card
EMV CAP is defined on top of EMV:
an EMV-CAP session is an aborted EMV session, where one of the cryptograms is used to construct the 8 digit response
internet banking
  Mastercard : CAP (Card Authentication Program)
  Visa : DPA (Dynamic Passcode Authentication)
e-commerce
  Mastercard: SecureCode
  Visa: Verified by Visa
EMV CAP specs are secret but have been largely reverse-engineered

## Slide 60: Limitations of EMV-CAP
EMV-CAP does not protect against e.g.
Man-in-the-Browser attacks,
  ie. malware inside the browser or on the user’s PC
Phishing attacks tricking customers to go to fake bank websites
Social engineering attacks by telephone on customers

## Slide 61: Internet banking fraud in Netherlands (millions euro)
[Source: Betaalvereniging]
After 2012, up to 2019, fraud under control thanks to
better monitoring - for suspicious transactions & money mules
  finding money mules, to extract money from the system without being caught, is the bottleneck for attackers
awareness campaigns
criminal switching to ransomware as better business model?
Notes: almost all of the current fraud is phishing

## Slide 62: Example attack on internet banking (1)
Your online bank statement shows you received 3000 euro from some company you never heard of
You get a phone call from the bank, saying that this is a mistake and asking you to transfer the money back
You never received 3000 euro, but malware in your browser inserts the fake transaction
  i.e. Man-in-the-Browser attack
When you transfer the money back, that is not a fake transaction…

## Slide 63: Example attack on internet banking (2)
Problem: Money trail no longer leads to criminal webshop, but to the innocent bitcoin shop
Root cause: messages to user not very informative, so user does not spot the attack
Solution: better monitoring, and banks impose extra rules on bitcoin shops & online casinos for allowing internet payments
victim
criminal web shop
bitcoin
web shop
bank
website
how much for an iPhone ?
200 €
cool, I want one
redirect to bank
200 € worth of bitcoin, please
redirect to bank
bitcoins

## Slide 64: Protocol flaw in EMV-CAP Mode 2
  user → reader : challenge
  reader → card : 0x000000
  card → reader : K ,
  where K = HMACKey(0x000000 ++ counter)
  reader displays some digits from {challenge}_K
So challenge C never goes to the card!
The message in step 2 is predictable so an attacker with temporary access to a card could harvest responses K to do internet banking later
  [P. Szikora and P. Teuwen, Banques en ligne: à la découverte d’EMV-CAP, MISC (Multi-System & Internet Security Cookbook) , 2011]

## Slide 65: Example attack on internet banking (3)
Security flaw in Gemalto e.dentifier2 for ABN/AMRO
  only when device is used with USB cable
Found during Master thesis project of Arjan Blom
    [A. Blom et al., Designed to Fail: A USB-Connected Reader for Online Banking NordSec 2012]
Bug now fixed, but old vulnerable devices not recalled

## Slide 66: Motivation for USB cable
Computer display of
cannot be trusted
(despite )
This reader can be trusted.
But can the user understand
the semantics of numbers?
→ 23459876
← 123654

## Slide 67: Motivation for USB cable
This display can be
trusted & understood
“What You Sign is
What You See”
(WYSIWYS)
USB

## Slide 68: Rabo Scanner
Alternative solution to allow communication to hand-held reader (with coloured QR code)
No communication back to the PC, unlike with USB cable

## Slide 69: Analysis of e.dentifier: first observation
Text for display goes in plain-text over USB line
So malware on the laptop can make the token show any message

## Slide 70: Reverse-Engineered Protocol
GENERATE AC f(number, text)
PC
reader
card
display:‘enter pin’
display:‘text’
user enters PIN
user presses OK
ASK-PIN
PIN-OK
SIGN (number, text )
USER-OK
COMPLETE
g(cryptogram)
cryptogram
PIN
OK

## Slide 71: Reverse-Engineered Protocol
GENERATE AC f(number, text)
PC
reader
card
display:‘enter pin’
display:‘text’
user enters PIN
user presses OK
ASK-PIN
PIN-OK
SIGN (number, text )
USER-OK
COMPLETE
g(cryptogram)
cryptogram
PIN
OK

## Slide 72: Attack!
GENERATE AC f(number, text)
PC
reader
card
display:‘enter pin’
display:‘text’
user enters PIN
user presses OK
ASK-PIN
PIN-OK
SIGN (number, text )
USER-OK
COMPLETE
g(cryptogram)
cryptogram
PIN
OK

## Slide 73: Problem with Todos/Gemalto e.dentifier2
[Arjan Blom et al.,
Designed to Fail: A USB-Connected Reader for Online Banking, NordSec 2012]
It’s possible to press OK via
USB cable...
Malware on an infected PC could change all the transaction details and press OK
Purely academic, no criminal ever abuses thus

## Slide 74: Conclusions

## Slide 75: Conclusions about EMV & banking world
EMV protocol suite is way too complicated too many options, written down in confusing way, without useful abstractions, without explaining security, ...
Banks - or their suppliers - routinely screw up security. Eg we saw
  DDA: why not let the card sign transactions if it can do RSA?
  backwards compatibility problems
  lousy random number generators in ATMs
  misconfiguration of contactless cards
  contactless terminal crashing on extended length APDUs
  protocol flaws in EMV-CAP mode 2 and e.dentifier2
  …
Technical flaws harmless if there is no good attacker business model. But always a public relations risk.
Bottleneck in security here: AUTHENTICATION

## Slide 76: Conclusions about the banking world
Not so clear who is taking responsibility for checking security
    The banks?
    Scheme holders such as MasterCard and Visa? EMVco?
    Their suppliers? (eg Gemalto, ST Microelectronics,...)
    The parties doing certification tests for scheme holders? (eg UL)
    The Dutch or European Central Bank?
Banks appear to assume - and trust - that others check the security!
Or maybe their employees are happy with Cover-Your-Ass security?

## Slide 77: Moral of the story
Keep it simple!
Protocols should only have one version/variant, namely the secure one!
Never assume that somebody else (eg. a vendor, Mastercard, Visa, ...) has checked that things are secure!

## Slide 78: Possible research ideas
What would a post-quantum version of EMV look like?
  The old-fashioned reliance on a shared symmetric key (still 3DES in some bank cards!) may turn out to be an advantage…
How do the security levels of mobile phone-based alternatives compare to smartcards?